## Slide 1
Design and Demonstration of an IoT System
Streaming motion and sound data from a microcontroller to a live dashboard
CSEE 8300 — Principles of Cyber-Physical Systems
Notes: One microcontroller, a small server, and a dashboard showing real sensor data.

## Slide 2
What I built
An IoT system that collects data from real sensors and displays it live
A M5StickC PLUS microcontroller samples motion and sound 50 times a second
Data travels over MQTT to a Ubuntu server, is stored in a time-series database, and is shown in Grafana
I wrote the device firmware, the program that moves data into the database, and the scripts that build the server
About 1,700 lines of code in C++, Python and shell
Notes: The sensors are real, not simulated — gravity and sound are genuinely measured.

## Slide 3
System architecture
M5StickC PLUS
2 sensors
MQTT broker
Mosquitto
Forwarder
Python
InfluxDB
storage
Grafana
dashboard
clock synchronisation (NTP)
The sensor gets its clock from the same server that stores its data
Each message carries one second of samples rather than one sample at a time
Notes: Left to right, then the dashed line: the server is also the time source for the board.

## Slide 4
Hardware and sensors
M5StickC PLUS
ESP32 processor, WiFi (2.4 GHz only)
1.14 inch display, 120 mAh battery
Costs about $20
Two sensors on the board
MPU6886 — accelerometer and gyroscope, sampled at 50 Hz
SPM1423 — microphone, sampled at 16,000 Hz
The microphone runs 320 times faster than the motion sensor. Sending that much raw audio would overwhelm the network and the database, so the board calculates the sound level itself and sends only that figure, 50 times a second — the same rate as the motion data.
Notes: Clearest example of edge processing: do the work on the device, send the conclusion.

## Slide 5
Two design decisions
1. Group samples into one message per second
Sending each sample separately would mean 50 messages every second
Grouping one second of samples into a single message reduces that to one
The server splits the message back into 50 individually timestamped readings
2. Keep the database index small
InfluxDB keeps an index entry for every unique combination of labels
Labelling messages with a counter would create a new entry every second
Storing the counter as a value instead keeps the index at 25 entries no matter how much data arrives
Notes: Both decisions matter only at scale — which is why they are made at the start.

## Slide 6
Keeping the clocks in step
A timestamp only means something if every part of the system agrees on the time.
The server synchronises itself to public internet time servers
The board then asks the server for the time, every 15 minutes
Sample timing uses the board's own hardware timer, so a clock correction cannot disturb data already being collected
When the board first connected, its clock was 887 milliseconds out. The system measured that correction and recorded it, rather than assuming the clocks agreed.
Notes: Wrong clocks do not error — they make data invisible, landing outside the window you view.

## Slide 7
Software on the server
Service | Purpose
chrony | Keeps time, and provides time to the board
Mosquitto | Receives messages from the sensor
InfluxDB | Stores the readings
MySQL | Holds device records and settings
Grafana | Displays the live dashboard
All five run on one Ubuntu virtual machine. Six scripts install and configure them, and each one checks its own work before the next runs.
Notes: Everything is scripted so the whole server can be rebuilt from scratch.

## Slide 8
Resource usage
Chart: 
| InfluxDB | MySQL | Grafana | Forwarder | Mosquitto | chrony
Memory (MB) | 286.8 | 185.7 | 63 | 27.6 | 6.7 | 4.6
The whole system uses about 600 MB of memory
InfluxDB accounts for nearly half of it, and almost all the processor time
Everything else is small by comparison, so tuning effort belongs in one place
The system measures its own resource use while running
Notes: Medians over a steady period, repeated three times, not single readings.

## Slide 9
Homework 1 — results
What works
Real motion and sound data arriving continuously
Laid flat, the board reads 1.0 g downward — gravity, and it moves between axes when the board is tilted
The board takes its time from the server, confirmed on the server's client list
A single command runs 13 checks across the system; all pass
Then: make it secure
Homework 1 ran fully open on a trusted network
Anyone on the same WiFi could read the data, or send fake data
Homework 2 closes those gaps — the next slides
The most useful lesson: a wrong clock does not cause an error message. It makes data quietly disappear.
Notes: This closes HW1 and sets up HW2 (security).

## Slide 10
Homework 2 — enhancing security
Homework 1 proved the system works. Homework 2 makes it safe to run on an untrusted network, and protects the code itself.
1. Encrypt the connection
MQTT now runs over TLS on port 8883. The board checks the server's certificate before sending anything.
2. Process the data
An AI framework analyses the live stream and the stored history, driven entirely by a configuration file.
3. Make the code unreadable
The Python programs are compiled into standalone binaries, so the source cannot be read back.
4. Make the code uncopyable
The binaries are encrypted with a key locked inside the machine's TPM chip, so a copied file is useless elsewhere.
Notes: Four requirements: TLS, the AI framework, Nuitka compilation, and TPM protection.

## Slide 11
Securing the connection
M5StickC PLUS
the sensor
MQTT broker
the server
encrypted (TLS, port 8883)
checks certificate
Before, messages travelled in plain text on port 1883 — anyone on the network could read or forge them
Now the broker presents a certificate signed by a private authority, and the board carries a copy of that authority
The board refuses to send data unless the certificate checks out, so it cannot be tricked by a fake server
Verified on the real hardware: the board validates the certificate and streams over the encrypted channel
Notes: A real debugging story: the ESP32 matched the server's IP against the wrong kind of certificate name; fixed by adding the IP in the expected form.

## Slide 12
Processing the data — AI framework
Live (MQTT)
real time
Stored (InfluxDB)
history
Shared analysis
one definition
Results
back to database
Two programs — one reads the live stream, one re-reads stored history for a chosen time range
Both share the same analysis code, so a measurement means the same thing live or after the fact
A configuration file decides which sensors and which calculations to run — nothing is fixed in the code
It correctly tracked the board moving between still, walking and shaking, labelling each automatically
Notes: The same framework the reference design reserved a place for; built in HW2. Config-driven: changing the YAML changes the output with no code change.

## Slide 13
Protecting the program
Two layers, answering two different threats.
Make it unreadable
The Python programs are compiled into standalone binaries
The original source code cannot be read back out of them
The binaries were checked to give exactly the same results as the source
Make it uncopyable
Each binary is encrypted with a key locked inside the machine's TPM security chip
The chip only releases the key on the machine that created it
Copying the file to another machine leaves it unusable — the other chip will not unlock it
Demonstrated: the protected program runs on its own machine, and the same files are refused on a machine with a different security chip.
Notes: Nuitka for unreadable; TPM-sealed AES key for uncopyable. Copy-protection proven with two TPM instances.

## Slide 14
Homework 2 — results
The real board now streams encrypted sensor data end to end, and still lands correctly in the dashboard
The AI framework processes both the live stream and the stored history, controlled entirely by a config file
The analysis programs run as compiled binaries whose output matches the source exactly
Those binaries are locked to their machine by the TPM — a copied binary will not run anywhere else
The system went from fully open to: encrypted in transit, configurable in processing, and protected at rest — without changing what it does.
Notes: All four HW2 requirements complete and verified on the real system.